## Slide 1
MOTION-BASED SMART LED LIGHTING SYSTEM

## Slide 2
INTRODUCTION
  Rapid growth in energy consumption demands efficient utilization of electrical power
  Conventional lighting systems result in significant energy wastage due to manual control
  Automation using sensor-based systems provides an effective solution
  The proposed system uses a PIR sensor to detect human motion based on infrared radiation
  A microcontroller processes the sensor signal and controls the LED accordingly
  The system automatically switches ON the light upon motion detection and OFF after a predefined delay
  Provides an energy-efficient, cost-effective, and reliable lighting solution for modern applications

## Slide 3
Motivation
  Need for energy-efficient lighting using motion detection and ambient light sensing
  Requirement of multi-level brightness control (100%, reduced, background)
  Overcome issues like false triggering and inefficient energy usage
  Demand for user-configurable automated lighting systems
Applications
  Smart lighting with motion + lux-based control
  Street and industrial lighting with adaptive brightness levels
  Security systems using motion-triggered illumination
Social Relevance
  Reduces energy consumption using PWM-based dimming and lux control
  Supports sustainable and smart infrastructure
  Enhances user convenience and automation

## Slide 4
Aim And Objective
  To study motion detection using PIR sensor and ambient light sensing using lux sensor for adaptive lighting control
  To design a system with multi-level brightness operation (Full, Reduced, Background) based on motion and timing logic
  To implement LED dimming using PWM and microcontroller-based control logic
  To develop a system with user-configurable parameters (brightness levels, lux threshold, delay timings T1 & T2)
  To test and evaluate system performance based on state-based operation (OFF, FULL, REDUCED, BACKGROUND) and energy efficiency
  To design and implement a motion-based LED lighting system with ambient light sensing, multi-level brightness control, and user-configurable operation

## Slide 5
Literature Survey
[1] IEEE Xplore, Smart Motion-Based Lighting Systems for Energy Efficiency, 2020
[2] Passive Infrared (PIR) Sensor Datasheet, HC-SR501 Module
[3] Ambient Light Sensor Datasheet (LDR / BH1750 Lux Sensor)
[4] Texas Instruments, LED Driver Design and PWM Dimming Techniques
[5] Arduino Documentation, Microcontroller Programming and PWM Control
[6] IEEE Xplore, Adaptive Lighting Control Using Motion and Ambient Light Sensors, 2021
[7] Espressif Systems, ESP32 Technical Reference Manual
[8] ON Semiconductor, Constant Current LED Driver Design Guide
[9] PIR Motion Sensor Datasheet (Detailed)
https://www.handsontec.com/dataspecs/SR501%20Motion%20Sensor.pdf
[10] HC-SR501 Complete Datasheet (Alt Source)
https://electronilab.co/wp-content/uploads/2013/12/HC-SR501.pdf

## Slide 6
Time Period Control Using Bluetooth
Purpose
  To allow wireless adjustment of T1 and T2 time periods
  To provide remote and user-friendly control
  To achieve higher precision compared to manual knobs
  To enable real-time parameter tuning without hardware changes
Working
  Bluetooth functionality is implemented using the ESP32.
  A mobile application sends digital time values for T1 and T2.
  The ESP32 receives these values wirelessly via Bluetooth.
  The received values are processed and mapped to internal timers.
  When Bluetooth is active, the digital values override rotor knob settings.
  Updated time periods are applied instantly during operation.
  Screen reader content is loading

## Slide 8
Time Period Control Using ROTOR
Purpose
  Used for manual adjustment of T1 and T2 time periods
  Provides user control without Bluetooth
  Allows quick and smooth tuning of delay values
  Time Period Control Using ROTOR
Working
  The rotor knob is a rotary potentiometer with three terminals: VCC, GND, and output.
  Rotating the knob changes the internal resistance.
  This causes a change in the output analog voltage.
  The ESP32 reads this voltage using its ADC.
  The ADC value is mapped to time delay values for T1 or T2.
  As the knob is rotated, the ON and OFF delay times increase or decrease accordingly.

## Slide 9
Time Period Control Using Bluetooth
Purpose
  To allow wireless adjustment of T1 and T2 time periods
  To provide remote and user-friendly control
  To achieve higher precision compared to manual knobs
  To enable real-time parameter tuning without hardware changes
Working
  Bluetooth functionality is implemented using the ESP32.
  A mobile application sends digital time values for T1 and T2.
  The ESP32 receives these values wirelessly via Bluetooth.
  The received values are processed and mapped to internal timers.
  When Bluetooth is active, the digital values override rotor knob settings.
  Updated time periods are applied instantly during operation.
  Screen reader content is loading

## Slide 10
LUX Control
Purpose
  To detect ambient light intensity in the surroundings
  To ensure LED operation only in low-light conditions
  To reduce unnecessary power consumption
  To improve energy efficiency and LED lifespan
Working
  A lux sensor (LDR or digital light sensor) is used to measure ambient light.
  The sensor output varies according to surrounding light intensity.
  The ESP32 reads the sensor value using an ADC (or digital interface).
  The measured lux value is compared with a preset threshold.
  If ambient light is below the threshold, the LED is allowed to turn ON.
  If ambient light is above the threshold, the LED remains OFF even if motion is detected.

## Slide 11
  The ESP32 stays in deep sleep mode to save power.
  The PIR sensor continuously monitors motion.
  When motion is detected, it sends a signal to the RTC GPIO pin.
  This triggers an external interrupt, waking up the ESP32.
  The ESP32 restores operation and runs the main program.

## Slide 12
Schematic Diagram

## Slide 13
Block Diagram

## Slide 14
Outcome of Literature Review
  Identified need for combined motion + lux-based control system [1][3]
  Existing systems showed false triggering and inefficient brightness control [1]
  Lack of multi-level brightness and user configurability in basic systems [1]
  Limitations Overcome
  Implemented multi-level brightness (Full, Reduced, Background) for better efficiency [1]
  Reduced false triggering using proper sensor interfacing and signal filtering [2]
  Improved system using PWM-based smooth dimming control [4]
  Added user-configurable parameters (T1, T2, brightness, lux threshold) [1]

## Slide 15
PCB Designs

## Slide 16
Testing & Debugging
Observed issues during testing:
  False triggering due to environmental noise [2]
  Incorrect brightness transitions [4]
  Delay mismatch in timing (T1, T2) [1]
Corrections Implemented:
  Adjusted PIR sensitivity and delay settings [2]
  Optimized PWM signal for smooth dimming [4]
  Calibrated lux threshold for accurate ambient sensing [3]
  Verified state transitions (FULL → REDUCED → BACKGROUND) [1]

## Slide 17
  PIR Motion Sensor (HC-SR501) [2]
  Ambient Light Sensor (LDR / Lux Sensor) [3]
  Microcontroller (Arduino / ESP32) [5]
  LED with constant current driver [4]
  Resistors, power supply, connecting wires
  IR receiver module (for user control – optional) [1]
  Optional: LDR(Ambient light control)
  Microcontroller (ESP32)
  LED & Driver Electronics
  High Power LED (9W)
  LED Constant Current Driver(300mA–700mA)
  PWM Dimming Interface (MCU → Driver)
  Resistors, capacitors, connectors, headers
Resources

## Slide 18
  Integration with IoT for remote monitoring and real-time control of lighting parameters [5]
  Implementation of AI/ML algorithms for adaptive brightness based on usage patterns
  Use of advanced motion sensors (microwave/mmWave) for higher accuracy and reduced false triggering [1]
  Development of self-learning systems to automatically adjust lux threshold and delay timings (T1, T2) [1]
  Integration with smart home systems (centralized automation platforms)
  Use of solar-powered LED systems for energy-efficient standalone operation
  Enhancement with wireless communication (Wi-Fi/Bluetooth) for user control [5]
  Expansion for smart street lighting with network-based centralized control [1]
Future Scope

## Slide 19
Conclusion
  The literature shows that conventional PIR lighting systems lack dimming, suffer
from flicker, and are less efficient. Using an efficient SMPS-based LED driver with
smooth, low-flicker dimming and intelligent control can significantly improve energy
efficiency and lighting quality.
  Literature is that abrupt ON/OFF switching in conventional systems causes sudden
changes in illumination, which can be uncomfortable for users. Gradual dimming and
soft-start techniques are recommended to improve visual comfort. Intelligent
control also helps reduce unnecessary power consumption during idle periods. This
approach supports longer LED life and better overall system reliability

## Slide 20
THANK YOU